## Slide 1: Performance optimization for modern many-core architectures using PSyclone embedded-DSL.
Sergi Siso (sergi.siso@stfc.ac.uk)
High-Performance Software Engineer
IPCC @ Hartree, STFC Daresbury Laboratory, United Kingdom
Work done with: Rupert Ford, Andrew Porter, Christopher Maynard

## Slide 2: Project Background
LFRic project
        Met Office (UK) project to develop a replacement for the Unified Model.
        Developed in a collaboration between MetOffice and STFC (Hartree Centre)
Named in honour of Lewis Fry Richardson (first numerical weather ‘prediction’)
Gungho project
MetOffice, NERC and STFC initial investigation and design for next-generation model. They produced a set or recommendations for LFRic.
New dynamical core more scalable and without the singularity on the poles:
  Mixed finite-element scheme with a cubed-sphere mesh.
Good software abstraction and separation of concerns.
Achieve good performance on current and future supercomputers.
Notes: Optimising UM is very labour intensive

## Slide 3: Separation of concerns
Natural Science Knowledge
Finite element/volume/difference-specific
Time-stepping
Operations over a mesh
Typically same operation at each element/volume/point
Computational Science Knowledge
Parallelism
Data decomposition
Data locality
Architecture/platform dependent optimizations
HPC Specialists
Domain Scientists
Notes: Data parallel (typically independent operations)
Nearest neighbour communications for stencils
Global reduction(s) for convergence and/or conservation

## Slide 4: PSyclone
Algorithm
Kernel
Parallel System
Computational Science
Natural Science
Operates on full fields
Operates on local elements or columns
Given domain-specific knowledge and information about the Algorithm and Kernels, the Parallel System layer can be generated by ...
Notes: A domain-specific source-to-source (Fortran -> Fortran) compiler for embedded DSL(s)
  Supports distributed- and shared-memory parallelism
  Reduces programmer errors (both correctness and performance) in implementing parallel code
  Optimisations encoded as a ‘recipe’ rather than baked into the scientific source code
  Different recipes for different architectures

## Slide 5: Hartree IPCC Contribution to PSyclone / LFRic
Explore the performance characteristics of LFRic / PSyclone on many-core architectures (Intel Xeon Phi x200)
Feedback the obtained knowledge to PSyclone and LFRic projects
PSyKAl
LFRic
Exploration on KNL platform
feedback
optimisations
input science
generates parallel system
Hartree – Intel PCC
Other platforms Other HPC experts

## Slide 6: Matrix Vector Multiplication Kernel (hotspot and representative kernel)
LFRic uses multiple FEM fields:
Operations are encoded in LMA (local matrix assembly) and are designed to transform from one field to another.
Very Small matrix-vector multiplication – difficult to optimise...
but we have many to do (horizontal and extruded dims) and they share data

## Slide 7
Original: LFRic current implementation. VTune pinpoints L2 Misses and SIMD-to-L2 ratio issues.
Fused & Interleaved: Fuse gathers, computation and scatters, do each FMA interleaved with next mv.
Loop K Inner: Refactor loops to go through vertical domain first.
DL K Contiguous: Refactor data layout.
Merge Inner Dofs: Update top dof of i layer at the same time as the bottom dofs i+1 layer.
(mkl and libxsmm couldn’t improve the performance of manual implementation)

## Slide 8: OpenMP Implementations
gungho-mv ‘DL K Contiguous’ implementation
Problem size: 32x32 (x16)
OMP Schedule: Static
OMP Affinity: Scattered
KNL: cache-quadrant
Thread oversubscribing helps across all implementations.
Colouring beats Locking for more than 10 threads.

## Slide 9: Skylake vs KNL vs KNL with MCDRAM
Best Performance
Vector Efficiency is ~ x2

## Slide 10: Skylake and KNL Rooflines
Full node mv-kernel for:
Skylake is at the DDR STREAM Triad boundary.
KNL is at 76% of MCDRAM STREAM Triad boundary.
Next step could be kernel-fusing:

## Slide 11: MPI Efficiency
Chart: MPI Ranks
| 192 | 768 | 3072
PSyclone1.6 | 1 | 0.68135 | 0.15459
annex_dofs | 1 | 0.67355 | 0.3794
gh_inc | 1 | 0.68529 | 0.21278
gh_inc+annex_dofs | 1 | 0.65989 | 0.36496

## Slide 12: Transparently apply PSyclone optimizations to Halo Exchanges
Original Optimized

## Slide 13: Future work
OpenMP strategies, loop fusions, halo exchange optimisations, … can be extended to the whole code with PSyclone.
However, changing the data layout and refactoring the loops is a manual process at the moment.
  IPCC recommends that PSyclone explores mechanisms to abstract the data layout (and/or loop structure).
  This is essential for achieving optimal performance.
LFRic is still in development: column matrix assembly, multi-grid and other features are coming.

## Slide 14
Hartree Evaluation Access Programme
Sergi Siso : sergi.siso@stfc.ac.uk
http://www.hartree.stfc.ac.uk
Thanks for your attention

## Slide 15: Annex Slides

## Slide 16: Hartree Centre Scafell Pike Systems
  ATOS Sequana x1000
  840 – 2 x Intel Xeon Gold E5-6142 v5 (formerly Skylake) 16 core up to 3.7GHz
  840 – self-hosted Intel Xeon Phi KNL 7210 nodes 64 cores up to 1.5 GHz
  27000 + 54144 cores
  Mellanox EDR Infiniband

## Slide 17: LFRic KNL VTune Analysis
Poor L2 usage
Poor Simd-to-L1/L2 ratios

## Slide 18: PSyclone architecture
PSy
Generator
Algorithm
Generator
Parser
Alg
Code
Kernel
Codes
PSy
Code
Alg
Code
Transforms
Transformation
psy
f90
f90
schedule
info
AST

## Slide 19: Algorithm Layer example

## Slide 20: Kernel Layer Example

## Slide 21: PSy generated code